## Slide 1: Riding Mechanic: An iOS App for Vehicle Monitoring and Analysis
Student Name: Dezheng Wang
Faculty Advisor: Dr. Elliott Forbes

## Slide 2: Introduction
Difficult to imagine life without driving.
On-Board Diagnostic (OBD) applications
Disadvantages of OBD applications in the market
Advantages of Riding Mechanic

## Slide 3: On-Board Diagnostic Systems (OBD)
Purpose of designing OBD
OBD-II
Unique features of OBD-II

## Slide 4: OBD-II Scanner
How an OBD-II scanner works
  Wi-Fi scanner and Bluetooth scanner
Reasons for choosing Wi-Fi scanner

## Slide 5: OBD-II Scanner
© Freelancer Technology Pty Limited

## Slide 6: Onboard Diagnostic Parameter IDs
OBD-II PIDs
  Ten modes
  PIDs used in this project
Mode (hex) | Description
01 | Show current data
03 | Show stored Diagnostic Trouble Codes

## Slide 7: PIDs Used in Project
OBD-II PIDs | Description
0100 | Get supported PIDs [01-20]
0120 | Get supported PIDs [21-40]
0140 | Get supported PIDs [41-60]
0105 | Get engine coolant temperature
010C | Get engine RPM
010D | Get vehicle speed
0110 | Get MAF air flow rate
0142 | Get control module voltage

## Slide 8: Diagnostic Trouble Code (DTCs)
  How characters are encoded
  Consist of five characters
  Each letter’s meaning
  DTCs in this project
Letter | System
P | Powertrain (Includes engine, transmission, drive shafts, differentials and the Final Drive)
U | User Network (Wiring Bus or UART)
B | Body (Includes A/C and Air Bag)
C | Chassis (Includes ABS)

## Slide 9: AT Command Set
  Hayes command set
  Compared to OBD-II commands
  AT commands used in this project
Version | Command | Description | Group
1.0 | @1 | Display the device description | General
1.3 | @2 | Display the device identifier | General
1.3 | SP 00 | Set protocol to auto and save it | OBD
1.0 | Z | Reset all | General

## Slide 10: Requirement Analysis
User requirements
  Users want to do
Functional requirements
  The system must have
Non-functional requirements
  The system should have

## Slide 11: A Simple Example
Index: Access.1
Name: Register
Purpose: To register an account for Riding Mechanic.
Input parameters: Username, password, confirm password
Action: Ensure that username doesn’t exist in the system.
Ensure that username is in email format.
Ensure that password or confirm password field should not be empty.
Ensure that password and confirm password are same.
Show information of registering an account successfully.
Output parameters: None
Exceptions: Username has already existed or username is not in email format
Password or confirm password is empty.
Password and confirm password are different.
Remarks: Application should show proper error message when users make mistakes.
Cross-references: None

## Slide 12: System Architecture
Goal
  Prototype: Incremental model
  Identify Key technical risks
Constrains
  OBD-II Wi-Fi scanner
  Can’t connect to the server

## Slide 13: Key Scenarios
  Download and upload user information
  Connect to scanner’s Wi-Fi
  Keep sending OBD-II PIDs
  Save trip information
  Search trip information
  Download and upload trip information

## Slide 14: Application Overview
Application Overview
  Combination architecture styles: client/server, object-oriented
  Tools and programming languages for server and client

## Slide 15
High Level Architecture

## Slide 16: Key Issues and Solutions
    Thread safety (UI, other activities)
    Extra data about the car

## Slide 17: Frequency of Sending Different OBD-II PIDs

## Slide 18: Key Values
How distance was calculated
How fuel cost was calculated
How sharp acceleration times and sharp braking times were calculated

## Slide 19: Detailed System Design
Database design
  User table
  Trip table
  Relationship between user table and trip table
  Password encryption and decryption

## Slide 21: Use Case Diagram

## Slide 22: Class Diagram

## Slide 23: Sequence Diagram

## Slide 24: GUI Design
User Interface design
  Tab bar
  Navigation bar
  Table view
  Alert

## Slide 25: Testing
Testing plan
  Server side, Postman
  Client side
  UI testing in Xcode

## Slide 26: Example
Test case # | Scenario | URL | Return value | Status
1 | User table has this account | 138.49.101.87:9000/userSettings /wang.dezheng@uwlax.edu Method: GET | All user information related to username ‘wang.dezheng@uwlax.edu’ | Passed
2 | User table doesn’t have this account | 138.49.101.87:9000/userSettings /wang.dezheng@uwlax.edu Method: GET | [] | Passed

## Slide 27
  Code Coverage

## Slide 28: Comparison

## Slide 29: Conclusion
Conclusion
  Achievement
  Defects
  Future Work

## Slide 30: Demo
Register, login, reset password
Start a trip, read real-time data, record a trip
Set speed alert, start a trip, record a trip
Search trip information
Read diagnostic trouble codes form the car